## Slide 1
Boundary Condition Map: Where BCs Enter the 2D Solver
First separate boundary conditions by physical location: electrode contacts, lateral domain edges, and internal material interfaces.
Takeaway: contact BC, lateral BC, and internal interface treatment are different objects and should not be explained in one crowded diagram.
HTL
absorber
ETL
2D drift-diffusion domain
Poisson: φ(0,x)=0, φ(Lᵧ,x)=Vᵦᵢ-Vₐₚₚ
carrier contacts: ohmic Dirichlet or Robin S
x=0
x=Lₓ
y transport direction
internal material interfaces
1. Contact BC
outer electrode rows
y=0 and y=Ly
controls carrier exchange
2. Lateral BC
left and right domain edges
periodic or Neumann
selected by lateral_bc
3. Interface Treatment
inside the stack
band offsets and recombination
not the same as contact BC
Fixed in 2D Poisson
φ=0 and φ=Vᵦᵢ-Vₐₚₚ
Dirichlet electrode potentials
Configurable in 2D Run
`lateral_bc`
periodic or neumann
used by Poisson + continuity
Configurable by S
Sₙ, Sₚ fields
missing: ohmic pin
finite: Robin contact
Notes: This opening slide is a location map. It deliberately avoids detailed formulas. The audience should first learn that SolarLab has three different BC-related concepts: contact boundary conditions at the electrodes, lateral boundary conditions at x edges, and internal interface treatment between layers.

## Slide 2
Contact Boundary Conditions: Ohmic, Blocking, and Robin
Contact BCs describe how the external electrodes exchange electrons and holes with the simulated device boundary rows.
Takeaway: SolarLab switches contact behavior through the S fields; missing S gives the ohmic Dirichlet pin, S=0 blocks flux, and finite S gives Robin selective contact.
Ohmic Dirichlet
missing or null S
electrode
semiconductor
fixed boundary value
BC equation
n=nₑq, p=pₑq
ideal carrier reservoir
boundary rows are pinned
RHS sets dn/dt and dp/dt to zero
Blocking Neumann
explicit S = 0
electrode
semiconductor
no flux
BC equation
Jₙ=0, Jₚ=0
no carrier flux through contact
boundary density can evolve
perfect blocking limit
Robin Selective Contact
finite S in mode=full
electrode
semiconductor
finite exchange
BC equation
Jcontact = ± q S (cₛ-cₑq)
finite exchange rate
matched carrier has large S
wrong-sign carrier has small S
SolarLab code mapping
Top/HTL: S_n_left, S_p_left Bottom/ETL: S_n_right, S_p_right Activation: mode = full
Notes: This is the contact BC slide. Explain that the figure is a local magnification of the electrode-device boundary, not the entire device. In SolarLab 2D, the same concept is applied along the full top and bottom boundary rows.

## Slide 3
Lateral Boundary Conditions: Periodic Cell vs Zero-Flux Wall
The lateral boundary controls what happens at x=0 and x=Lx; it is selected by the 2D run parameter lateral_bc.
Takeaway: periodic represents a repeating lateral unit cell, while Neumann represents a closed sidewall with zero normal flux.
Periodic Lateral Boundary
lateral_bc="periodic"
HTL
absorber
ETL
right edge wraps to left edge
Physical interpretation
simulate one representative lateral period; no artificial sidewall is introduced
Neumann Lateral Boundary
lateral_bc="neumann"
HTL
absorber
ETL
Jₓ=0
Jₓ=0
Physical interpretation
simulate an isolated lateral window; no carrier current or electric displacement leaves through sidewalls
Solver usage
The same lateral_bc is passed into Poisson assembly and continuity divergence for a consistent x-edge convention.
Notes: This slide should be very simple. The audience only needs to know that lateral_bc is a domain-edge choice. It is not the electrode contact model.

## Slide 4
Internal Material Interfaces: Not the Same as Contact BC
Internal interfaces occur between layers such as HTL/absorber or absorber/ETL; they modify transport inside the device rather than at the external electrode.
Takeaway: contact BC is an outer-boundary exchange model; internal interfaces are handled through band-offset-aware fluxes, thermionic capping, and optional interface recombination.
Local view around an internal interface
Material 1
interface region
Material 2
p(y)
n(y)
interface flux
interface flux
carrier density
y transport coordinate
What this slide is about
internal layer-layer interface
inside the device domain
not the metal electrode contact
Transport treatment
SG flux uses electron-affinity and bandgap offsets
thermionic-emission capping can limit large interface fluxes
Recombination treatment
1D path supports interface recombination velocities; 2D Stage-B focus uses material maps and interface-aware fluxes.
Do not label this as contact BC unless the interface is the external electrode.
Notes: This slide responds to the reference figure. The reference figure is best interpreted as an internal interface transport model, not as SolarLab's outer contact BC. Use it after the contact and lateral BC slides to avoid mixing concepts.