## Slide 1
2D RHS Assembly: From Carrier Fields to Time Derivatives
The semi-discrete operator F(Y) evaluated repeatedly inside the Radau transient solver.
Animated RHS pipeline
10 stages, 5 s per stage
Y -> rho -> phi -> R,G -> SG fluxes -> div J -> dn/dt, dp/dt -> dY/dt
Note: the GIF is a conceptual visualization of the code path, not a literal simulation snapshot.
INPUT STATE
Y = [ n(y,x), p(y,x) ]
COUPLED PHYSICS
rho -> phi by Poisson
G - R source/sink terms
J_n, J_p from Scharfetter-Gummel fluxes
OUTPUT RHS
dY/dt = [ dn/dt, dp/dt ]
Core equations
∇·(ε∇φ) = −ρ
∂n/∂t = (1/q)∇·Jₙ + G − R
∂p/∂t = −(1/q)∇·Jₚ + G − R
Takeaway: RHS assembly is the physics-numerics operator F(Y); Radau repeatedly calls it to advance the 2D drift-diffusion-Poisson system in time.
Notes: Suggested narration: 1. The 2D state Y stores all electron and hole densities on the lateral-stack grid. 2. RHS assembly unpacks Y, computes charge density, and solves Poisson for the electrostatic potential. 3. Generation and recombination provide local source and sink terms. 4. Scharfetter-Gummel fluxes compute drift-diffusion currents on grid faces. 5. Current divergence plus G-R gives dn/dt and dp/dt. 6. Contact boundary conditions are applied before packing the result as dY/dt. 7. Radau calls this operator many times during one transient settle step at a fixed applied voltage.