## Slide 1
Initial Condition: A Physically Prepared Starting State
SolarLab does not start from arbitrary carrier values; it first constructs a stable device state before transient solving.
A. What the Solver Needs
STATE VECTOR
The transient solver needs carrier and ion densities at t = 0.
1D: Y = [n, p, P]
2D: Y = [n(y,x), p(y,x)]
WHY IT MATTERS
A poor initial state creates artificial transients or stiff solver failure.
B. Preparation Logic
1
dark quasi-neutral state
2
optional light-soaked state
3
transient J-V solve
DARK RUN
Use the dark equilibrium directly.
ILLUMINATED RUN
First settle carriers under light, then start the voltage sweep.
less artificial transient
better Radau start
physical memory
Takeaway: initial condition is a pre-conditioned physical state, not a random numerical guess.
Notes: Suggested narration: Initial condition means the state given to the transient solver at t=0. In SolarLab this state is not arbitrary. The code prepares a dark quasi-neutral state first. For illuminated simulations it then allows carriers to settle under light before the actual J-V sweep starts. This avoids mixing an artificial dark-to-light transient into the intended voltage-sweep dynamics.

## Slide 2
1D Initial Condition: Dark Equilibrium and Light-Soaked State
The 1D solver prepares n(x), p(x), and the initial ion profile before running the voltage sweep.
A. Dark Quasi-Neutral Equilibrium
CARRIER BALANCE
n p = nᵢ² n - p = Nᴰ - Nᴬ
Local mass action plus approximate charge neutrality.
ION BACKGROUND
P = initial ion profile
configured from the device stack
used as the initial ionic background
CONTACT PINNING
n, p at contacts → equilibrium values
B. Illuminated Pre-Settle
dark state
Ydark
turn on light
G > 0
steady state
Ylight
SHORT TRANSIENT SETTLE
Ylight = Radau(Ydark, 10⁻³ s)
Carriers relax quickly; ions move little.
J-V WARM START
Each voltage point starts from the previous settled state, so device memory is preserved.
Takeaway: 1D starts from quasi-neutral dark equilibrium; illuminated runs first settle carriers under light.
Notes: Suggested narration: For the 1D system the state contains electrons, holes, and ions. The dark initializer solves a local analytic balance: mass action np=ni^2 and quasi-neutrality n-p=ND-NA. The ion density is initialized from the configured P_ion,0 profile. For illuminated J-V the code integrates from this dark state under light for a short time, producing a light-soaked carrier state before the voltage sweep. The sweep itself is warm-started point by point.

## Slide 3
2D Initial Condition: Extrude the 1D State into a 2D Mesh
The 2D solver starts laterally uniform, then lets grain boundaries and lateral BCs shape the transient solution.
A. 1D Seed on the y Grid
HTL
absorber
ETL
known 1D profiles: n(y), p(y), P(y)
B. Broadcast into 2D
optional GB
x
y
CARRIERS
copy n(y) across x
copy p(y) across x
IONS
freeze P(y)
into Poisson
Takeaway: 2D begins as a laterally uniform extrusion of the 1D prepared state; 2D physics then creates lateral variation.
Notes: Suggested narration: The 2D solver does not invent a separate arbitrary 2D initial state. It first solves the corresponding 1D problem on the same vertical y-grid. The electron and hole profiles are copied across the lateral x direction, producing a laterally uniform initial state. The ion profile is not dynamic in the current 2D Stage-A/B solver; it is frozen into the Poisson background as P_static. Grain boundaries and lateral boundary conditions affect the subsequent transient evolution, not the initial copy operation itself.