## Slide 1
2D Lateral BC: Periodic Window and Zero-Flux Sidewalls
The lateral BC closes the finite x-window of the 2D mesh; it is not an electrode contact condition.
A. Periodic Lateral Boundary
GB
wrap face flux
x = 0
x = Lx
MEANING: Left and right sides are copies of a repeating unit cell.
B. Neumann / Zero-Flux Sidewalls
closed sidewall
closed sidewall
Jₓ = 0
MEANING: Exterior side flux is zero; carriers do not leak out laterally.
C. What Changes in RHS Assembly
PERIODIC: add SG wrap flux at x sides
NEUMANN: set exterior side flux to zero
INTERIOR: interior physics unchanged
Takeaway: periodic BC makes a repeating 2D unit cell; Neumann BC closes the sidewalls with zero lateral flux.
Notes: Suggested narration: This slide should be read as the lateral counterpart to the external contact slide. The lateral boundary condition does not model electrodes. It closes the finite computational window in the x direction. Periodic BC connects the left and right sides with a wrap face, so flux leaving one side enters the other side. Neumann BC instead sets the exterior side flux to zero. The interior Scharfetter-Gummel face fluxes and recombination terms are unchanged; only the side-boundary divergence bookkeeping changes.