## Slide 1
Implicit Radau Time Integration of the Semi-Discrete 2D Drift-Diffusion System
Outer solver at fixed Vapp; repeatedly evaluates the RHS operator F(Y) until a quasi-steady carrier state is reached.
Outer Solver: Voltage-Specific Transient Settle
INPUT
Y0, Vapp
INITIAL-VALUE PROBLEM
dY/dt = F(Y; Vapp)
RADAU TRANSIENT SOLVE
implicit time stepping Y0 -> Y(tend)
SETTLED STATE
Y(tend)
quasi-steady n, p
OUTPUT
J(Vapp)
terminal current
t0
t1
...
tN
tend
Inside One Radau Step
Radau is an implicit Runge-Kutta method.
implicit stage equations
Ki = F(tn + ci h, Yn + h Σj aij Kj)
Yn+1 = Yn + h Σi bi Ki
stage evaluations call F(Y)
K1
K2
K3
INNER RHS OPERATOR
F(Y): Poisson + R/G
+ SG flux divergence
+ contact BCs
WHY IMPLICIT?
stiff transport
strong coupling
stable larger steps
run_transient_2d(...)
solve_ivp(method='Radau')
Takeaway: RHS assembly defines F(Y); Radau repeatedly evaluates F(Y) to advance the stiff 2D carrier-transport system toward a Vapp-specific quasi-steady state.
Actual J-V sweep mode: stepwise transient sweep. Hold Vk fixed on [tk, tk+1]; Radau advances Yk -> Yk+1. Δt = |Vk+1 - Vk| / scan rate; forward 0 -> Vmax, then reverse Vmax -> 0.
Notes: Suggested narration: This slide explains the outer time-integration layer of the 2D solver. After spatial discretization, the coupled drift-diffusion-Poisson PDE system becomes a stiff semi-discrete initial-value problem, dY/dt = F(Y; V_app), where Y contains all electron and hole densities on the 2D grid. The previous RHS assembly slide explains how F(Y) is constructed from Poisson, recombination, generation, Scharfetter-Gummel fluxes, and boundary conditions. Here, Radau uses that F(Y) inside an implicit time-stepping scheme. At each time step, Radau solves coupled nonlinear stage equations K_i, and each stage evaluation calls the RHS operator. For one fixed applied voltage V_app, the transient solver advances Y from the initial state Y0 to a settled or quasi-steady state Y(t_end). The terminal current J(V_app) is then extracted from the final spatial snapshot. This is why the RHS assembly is the inner kernel, while Radau is the outer solver that actually advances the system in time. In the current frontend J-V sweep, this fixed-voltage transient solve is chained across voltage samples rather than solved as a continuous voltage ramp. The backend holds V_k fixed for one Radau interval, computes dt = |V_{k+1} - V_k| / scan_rate, carries the final state Y_k forward to Y_{k+1}, and then repeats this from 0 to V_max and back from V_max to 0. Therefore the scan rate changes the physical dwell time per voltage step and can affect hysteresis. Academic phrasing: The spatially discretized 2D drift-diffusion-Poisson equations form a stiff semi-discrete ODE system. The RHS operator F(Y) is assembled at each nonlinear stage evaluation, and the initial-value problem is advanced using an implicit Radau IIA time integrator.