## Slide 1
External Contact BC: Ohmic Pinning and Selective Robin Flux
External contacts are electrode reservoirs at the top and bottom rows; they set how carriers enter or leave the 2D domain.
A. Contact Rows in the 2D Device
top electrode reservoir
HTL / contact layer
absorber
ETL / contact layer
bottom electrode reservoir
carrier exchange
carrier exchange
contact rows: y = 0 and y = Ly
B. Boundary Model Used by the RHS
OHMIC / DIRICHLET LIMIT
n = neq p = peq
Ideal reservoir: boundary carrier densities are pinned; the contact rows are not time-evolved.
SELECTIVE / ROBIN CONTACT
Jₙ = q Sₙ(n - neq) Jₚ = q Sₚ(p - peq)
Finite surface velocity S controls carrier exchange with the electrode reservoir.
S = 0
finite S
S -> infinity
blocking
selective
ohmic
Takeaway: external contact BCs model carrier exchange with electrodes; Dirichlet pins densities, Robin uses finite surface velocity S.
Notes: Suggested narration: This slide separates the physical location of the contact boundary from the mathematical boundary model. The contacts live at the top and bottom rows of the 2D mesh. In the ohmic Dirichlet limit, the electrode is treated as an ideal reservoir and the boundary carrier densities are pinned to equilibrium values. In the selective Robin formulation, the contact current is proportional to the difference between the boundary carrier density and its equilibrium reservoir value. The parameter S is a surface recombination or exchange velocity: S = 0 is blocking, finite S is selective, and very large S approaches the ohmic limit.