## Slide 1
2D Internal Interface: Band-Offset-Aware SG Face Flux
The interface is an internal finite-volume face: band parameters create a jump in the SG driving potential, and the resulting face flux enters the divergence conservatively.
A. Internal Face in the 2D Grid
y-direction
Material A, row j
Material B, row j+1
state: (n, p, φ) at row j
state: (n, p, φ) at row j+1
internal face f
J
n,f
,
J
p,f
shared normal flux
Numerical meaning: one shared face flux couples the two control volumes and enters their divergence balances with opposite signs.
B. Heterojunction Physics
energy
EC
EV
face f
ΔEC
ΔEV
Δψn,f = Δφf + Δχf
Δψp,f = Δφf + Δχf + ΔEg,f
Band offsets become SG driving-potential jumps.
C. Numerical Treatment
RHS path
POISSON FIELD
solve φ from charge density ρ
BAND-OFFSET DRIVING POTENTIALS
ψn = φ + χ
ψp = φ + χ + Eg
FACE JUMP ENTERS SG EXPONENT
ξn,f = Δψn,f/VT
ξp,f = Δψp,f/VT
BERNOULLI SG FACE FLUX
J
n,f
,
J
p,f
via B(ξ)
CAP + DIVERGENCE
|JSG| ≤ |JTE| if needed; then ∇·J
not BC
internal flux
Takeaway: band parameters χ and Eg turn offsets into SG driving-potential jumps; Bernoulli flux plus cap gives a conservative face current.
Notes: Suggested narration: This slide should replace the earlier carrier-density-curve sketch. The 2D code represents a material interface as an internal y-face between two neighboring finite-volume rows, not as a separate contact boundary condition. The left panel emphasizes the stencil: one face flux J_n,f and J_p,f couples row j and row j+1. The middle panel shows the heterojunction physics: chi and Eg change across the interface, producing conduction- and valence-band offsets. Those offsets enter the SG driving-potential jump: Delta psi_n,f = Delta phi_f + Delta chi_f and Delta psi_p,f = Delta phi_f + Delta chi_f + Delta E_g,f. The right panel maps this to the code path: Poisson gives phi, material arrays give chi and Eg, the solver constructs psi_n = phi + chi and psi_p = phi + chi + Eg, SG uses xi = Delta psi / V_T inside the Bernoulli flux, and thermionic-emission capping is applied at heterofaces when needed. The same face flux then enters the finite-volume divergence on the two sides with opposite signs, which is the conservative coupling.