## Slide 1
SCAPS-1D Input Parameters
Main editable inputs used to define a one-dimensional thin-film solar-cell simulation
Input block
Typical parameters
Physical role
Cell / stack
layer order, thickness d, area A, temperature T
1D geometry and operating temperature
Layer material
Eg, χ, εr, NC, NV, vth,n, vth,p
band alignment, electrostatics, carrier statistics
Transport
μn, μp, NA, ND; grading P(x) or P(y)
drift-diffusion mobility and fixed doping
Recombination
Brad, Cn/Cp, bulk defects Nt, Et, σn/σp
SRH / radiative / Auger loss channels
Interface
interface defects, tunneling, me, mh
heterojunction recombination and tunneling
Contacts
work function Φm or flat-band; Sn, Sp; optical filter
boundary carrier extraction and optical loss
Optical input
spectrum, illumination side, R/T, absorption α(λ)
generation profile G(x)
Simulation setup
working point V, f, T; J-V / C-V / C-f / QE ranges; mesh settings
defines which measurement is solved
SCAPS-1D input = device structure + material/defect physics + contact/optical conditions + measurement setup
Notes: Suggested narration: This slide compresses the SCAPS-1D input space into the blocks a beginner should recognize first. The cell stack defines the one-dimensional geometry; layer material and transport parameters define band alignment and drift-diffusion behavior; recombination and interface parameters define loss channels; contact and optical inputs define boundary extraction and generation; finally, the simulation setup tells SCAPS which measurement, such as J-V, C-V, C-f, or QE, to solve.